## Slide 1: Computational Neuroscience, Neurotechnology and Neuro-inspired Artificial Intelligence (ISRC-CN3) Building Reliable and Secure Embedded Systems with Neuromorphic Computing
Jim Harkin
Intelligent Systems Research Centre
Ulster University, Magee Campus, Co. Derry

## Slide 2: Content
Brain-inspired Hardware
Reliability via Self-repair (the concept)
Building Self-repairing Hardware
On-chip Communication Challenge and NoC Solution
Reliability Challenge
The Opportunities
Brain-inspired Information Processing

## Slide 3: Motivation
  Reliability is a significant challenge for modern electronic systems.
  Increased physical defects in advanced silicon manufacturing processes; wear-out faults etc. Permanent, Temp. (SEU, Electromagnetic Interference)
IEEE International Roadmap for Devices and Systems (IRDS), 2020
“With device feature sizes projected to decrease to less than 5 nm within the next 10 years, scaling as we know it is expected to soon reach its physical limits or get to a point where cost and reliability issues far outweigh the benefits.”
IEEE International Roadmap for Devices and Systems (IRDS), 2020

## Slide 4: Electronic Faults
Faults can be transient (disappear after a relatively short time), intermittent (cycle between events) or permanent (always present).
  Shrinking feature size
  Increasing number of faults manifesting post fabrication
  Wear-out faults
  Failure due to Aging
  Need for fault-tolerance or self-correcting strategies.
Multiplexer select lines can get corrupted
Transistor charge perturbed
Thermal overstress
Excess heat— melts materials, warps and breaks semiconductor dies.
Electrical overstress
High voltage transient at base can damage transistor creating a base-emitter short circuit.
MEAN time between failures (MTBF)
M. Ansari et al., IEEE Transactions on Emerging Topics in Computing 2021

## Slide 5: Electronic Faults
  Roller-coaster curve of the hazard rate
Bathtub model of hazard rate
A. Gaonkar, et al., "An Assessment of Validity of the Bathtub Model Hazard Rate Trends in Electronics," in IEEE Access, vol. 9, pp. 10282-10290, 2021
Source: Adrian Stoica, NASA
Source: Adrian Stoica, NASA

## Slide 6: Electronic Faults
  Roller-coaster curve of the hazard rate
Exposure to radiation can cause SEU
Bathtub model of hazard rate
A. Gaonkar, et al., "An Assessment of Validity of the Bathtub Model Hazard Rate Trends in Electronics," in IEEE Access, vol. 9, pp. 10282-10290, 2021
Source: Adrian Stoica, NASA
Source: Adrian Stoica, NASA
http://www.spaceweather.com/

## Slide 7: Self-X
  Traditional approaches: redundancy/replication models, error correction techniques, radiation hardening, Evolutionary/reconfigurable.
  Limited levels of reliability – constraints on:
  number of faults that can be tolerated (degree)
  level of granularity with which repairs can be implemented
  Often a central repair mechanism not distributed, therefore fault-prone
self-monitor
self-detect
self-repair
Self-X

## Slide 8: Operation of Fault Tolerant Systems
There are several key areas in the development of fault tolerant hardware computing systems:
Fault monitoring/detecting
- be able to detect a fault has occurred
Fault test and diagnostics
- where the fault is located
- the type of fault (transient, temporary or permanent)
Fault tolerant decision
- what can be done to restore the system’s operation, i.e. how can the fault be tolerated.
Monitor
Test
Diagnostics
Decision
Fault detected
Fault diagnosis made
Decision made on restoration
Not completed
Yes
Yes
Yes
Yes
No

## Slide 9: Mitigating Hardware Faults
There are several further strategies to mitigating faults:
  Fault tolerant hardening
  - Fault tolerant redundancy (dynamic)
  Fault tolerant replication (static)
Three main redundancy techniques used to creating fault-tolerant (FT) systems:
  - Hot Standby
  - Cold Standby
  - Warm Standby

## Slide 10: FT Redundancy : Hot Standby
Efficient and quick response time of the backup module
The strict synchronization requirement creates an overhead, i.e. wastage of resources.
The backup also has to be online with the primary.
Required: Complete Synchronization between the active and the backup components.
A
A
Active (primary)
Backup
(Duplication of component A)
Data in
Israel Koren, C. Mani Krishna, "Fault-Tolerant Systems", MK 2010

## Slide 11: FT Redundancy : Cold Standby
The solution is not synchronous.
It is not required to have the secondary online; it can be used for other processing as long the active is alive. Can save power!
It takes longer to recover from a fault.
Storage device is required.
The active component receives the incoming traffic updating the
internal state changes to a
reliable storage medium.
Only when the active fails is the backup updated with the state information.
A
A
Active (primary)
Backup
(secondary)
(Duplication of component A)
State updates
Storage
Israel Koren, C. Mani Krishna, "Fault-Tolerant Systems", MK 2010

## Slide 12: FT Redundancy : Warm Standby
The secondary can remain offline until the primary fails. Is suited to systems where the changes between states are infrequent.
Check-points are used as reference points; when the active fails, the secondary takes over and starts computing from the last check point. Data can be lost as only data is recorded from the last check-point.
The secondary is not in synchronisation with the active (as in the hot scenario)
However, it is not completely unaware of current activities of the active component
Check-pointing is used
Periodic state updates
A
A
Active (primary)
Backup
(secondary)
(Duplication of component A)
State updates
Storage
Data in
Israel Koren, C. Mani Krishna, "Fault-Tolerant Systems", MK 2010

## Slide 13: Fault-Tolerant Replication
Additional computing resources (hardware) are required.
Replication looks at creating several identical copies of the ‘mission’ system.
Aims to provide better detection of faults (better reliability!)
m=3

## Slide 14: Triple Modular Redundancy (TMR)
Triple Modular Redundancy (TMR) uses three (replicas) copies of the target system and detects incorrect behaviour (faults) by comparing all three outputs.
The faulty system is then masked and one of the two fault-free systems takes over.
A
A
Voter
Detect faults
Data in
B
C
All three systems are performing the same identical tasks (B and C are replicas of A)
Voter detects which one of the system produces an output different from the other two

## Slide 15: Detecting and Tolerating Faults
The fault is detected by voter and it is masked.
The system continues without interruption, i.e. it tolerates the fault by relying on A and C to take over.
A
A
Voter
Detect faults
Data in
B
C
Faulty
Voter detects B as faulty because it produced a different output value from A and C.
B is now masked and disconnected from the voter
Israel Koren, C. Mani Krishna, "Fault-Tolerant Systems", MK 2010

## Slide 16: Detecting and Tolerating Faults
The fault is detected by voter and it is masked.
The system continues without interruption, i.e. it tolerates the fault by relying on A and C to take over.
A
A
Voter
Detect faults
Data in
B
C
Faulty
B is now masked and disconnected from the voter
What happens if the voter becomes faulty?
Faulty
Voter detects B as faulty because it produced a different output value from A and C.

## Slide 17: Intelligent Self Repair
To date case-based reasoning (CBR) and genetic algorithms (GAs) have been used to drive the decision making process.
Selection of New Generation
Crossover
/
Mutation
Fitness evaluation
(evaluate decision criteria)
Initial population of repair
solutions
Create new FPGA mapping
Implement the repair
Yes
Stopping
Criteria
?
No
(Optimum solution found)
(Info from diagnostic process)
Intelligent Repair
(decision making)
GA iterates to find a good solution which will repair the system and meet any real-time performance constraints, access to I/O, minimise system computing delays etc.

## Slide 18: Challenges
  Low number of faults that can be tolerated
  Coarse level of granularity
  Central repair mechanism (fault-prone)
self-monitor
self-detect
self-repair
Self-X

## Slide 19
Brain-inspired Hardware
Reliability via Self-repair (the concept)
Building Self-repairing Hardware
On-chip Communication Challenge and NoC Solution
Reliability Challenge
The Opportunities
Brain-inspired Information Processing

## Slide 20
Taxonomy of AI
Artificial Intelligence
Next Computing and Engineering Wave
"A State-of-the-Art Survey on Deep Learning Theory and Architectures", Electronics 2019, 8, 292.
ML: Machine Learning
NN: Neural Networks
DL: Deep Learning
SNN: Spiking Neural Networks
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 21
CNN/DNN – popular in image recognition/speech processing, machine translation.
Artificial Intelligence
Source: "Understanding Deep Learning: DNN, RNN, LSTM, CNN and R-CNN" (2019)
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 22
Artificial Intelligence
Source: "MLPerf Inference Benchmark“, https://mlperf.org/ (2020)
Md Zahangir Alom, Electronics, 2019 (doi:10.3390/electronics8030292)
IEEE International Roadmap for Devices and Systems (IRDS), 2020

## Slide 23
Artificial Intelligence
Embedded AI (Hardware)
Acceleration of network inference and/or training
Low power
  Movidius Myriad 2 - Deep learning
  Huawei’s Neural Processing Unit (NPU) (Kirin 970)
  ARM Ethos-U55 NPU (Edge AI - CortexM55)
  Google Pixel Neural Core (Google Pixel)
  Qualcomm Hexagon DSP (AI Engine\Snapdragon 865)
  Habana Labs Gaudi and Goya neural processors (replaces Nervana)
(2017) https://medium.com/@shan.tang.g/a-list-of-chip-ip-for-deep-learning-48d05f1759ae
Xilinx/Altera FPGAs
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 24
Artificial Intelligence
Embedded AI (Hardware)
Acceleration of network inference and/or training
Low power
  Movidius Myriad 2 - Deep learning
  Huawei’s Neural Processing Unit (NPU) (Kirin 970)
  ARM Ethos-U55 NPU (Edge AI - CortexM55)
  Google Pixel Neural Core (Google Pixel)
  Qualcomm Hexagon DSP (AI Engine\Snapdragon 865)
  Habana Labs' Gaudi and Goya neural processors (replaces Nervana)
(2017) https://medium.com/@shan.tang.g/a-list-of-chip-ip-for-deep-learning-48d05f1759ae
Xilinx/Altera FPGAs
New kids on the blocks.
Cerebras (CS-1) process ~1.2 terabytes of data per second
Graphcore ( Colossus GC2) x100 over CPU/GPU
Groq (Tensor Stream Processor) 250 trillion FLOPS
Hailo (Hailo-8) penny-sized + outperformed Nvidia’s Xavier AGX
Syntiant (NDP100\NDP101) 140 µW x20 throughput over low-power MCUs
Tenstorrent (Grayskull)
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 25
Artificial Intelligence
Neuromorphic Computing?
Image: Oak Ridge Labs (2020)
1990
1990-mid
2000’s
Late 2000/2010
Present
Catherine Schuman, "NEUROMORPHIC COMPUTING: PAST, PRESENT, AND FUTURE", DATE 2020
Carver Mead “Neuromorphic electronic systems” (1990)
Much lower power
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 26
Artificial Intelligence
Neuromorphic Computing?
Intel’s neuromorphic computing (Loihi) 130 million synapses (x1,000 speedup/CPU) On-chip learning.
IBM Neural network processors (TrueNorth) 4,096 core, 256 million synapses
University of Manchester (SpiNNaker)
Heidelberg University (BrainScaleS)
Speedup >1,000 biological time
∼ 1011 neurons
∼ 1015 synapses
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 27
Artificial Intelligence
Neuromorphic Computing?
Speedup >1,000 biological time
Bipin Rajendran, "Low-Power Neuromorphic Hardware for Signal Processing Applications", IEEE Signal Processing Magazine 36(6) Nov. 2019
Intel’s neuromorphic computing (Loihi) 130 million synapses (x1,000 speedup/CPU) On-chip learning.
IBM Neural network processors (TrueNorth) 4,096 core, 256 million synapses
University of Manchester (SpiNNaker)
HeidelBerg University (BrainScaleS)
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 28
Artificial Intelligence
Neuromorphic Computing?
Speedup >1,000 biological time
Bipin Rajendran, "Low-Power Neuromorphic Hardware for Signal Processing Applications", IEEE Signal Processing Magazine 36(6) Nov. 2019
Intel’s neuromorphic computing (Loihi) 130 million synapses (x1,000 speedup/CPU) On-chip learning.
IBM Neural network processors (TrueNorth) 4,096 core, 256 million synapses
University of Manchester (SpiNNaker)
HeidelBerg University (BrainScaleS)
GrAI Matter Labs (GrAI One) 35mW @ 25 MHz, 200K neurons
BrainChip (SoC Akida) 1.2 million neurons + 10 billion synapses
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 29
Artificial Intelligence
Are we there yet?
  Some way to go
  Current AI – had IQ of a 6 year old!
  Feng Liu et al. “Intelligence Quotient and Intelligence Grade of Artificial Intelligence” (2016). Carried out tests ranking Google’s AI IQ at 47.2, just shy of the average IQ of a 6-year-old.
Notes: When we hear of AI we tend to think of terminator, I-Robot
The fully thinking machine (human like is some way off)
But AI is used in a vast range of narrow specialist areas

## Slide 30: Unmet Need
  Look to mimic fault-tolerant capability of the human brain (to a degree) to build reliable computing hardware.
We can learn a lot from biology, in particular neuroscience!
Brain processing : robust and power-efficient information computing.
Exploit the brain’s self-repair mechanism (astrocyte cells)
Aim to develop astrocyte-neuron networks……. “Self-rePAiring spiking Neuron NEtwoRk” (SPANNER)
Brain employs a massively parallel computational network comprising of ∼ 1011 neurons and ∼ 1015 synapses.

## Slide 31: Brain-Inspired Data Processing
Spiking neural network (SNN) a more biologically plausible model of the brain – a neural computing paradigm.
Output
Input
Reads I/P patterns and classifies with an O/P pattern
Data
representation

## Slide 32: Brain-Inspired Data Processing
Spiking neural network (SNN) a more biologically plausible model of the brain – a neural computing paradigm.
Output
Input
Reads I/P patterns and classifies with an O/P pattern
Data
representation

## Slide 33: Brain-Inspired Data Processing
Spiking neural network (SNN) a more biologically plausible model of the brain – a neural computing paradigm.
Output
Input
Reads I/P patterns and classifies with an O/P pattern
Data
representation
CD Schuman, "A survey of neuromorphic computing and neural networks in hardware", 2017

## Slide 34
Brain-inspired Hardware
Reliability via Self-repair (the concept)
Building Self-repairing Hardware
On-chip Communication Challenge and NoC Solution
Reliability Challenge
The Opportunities
Brain-inspired Information Processing

## Slide 35: More Knowledge on Brain Repair
  Nicola J. Allen & Ben A. Barres, "Glia — more than just brain glue," Nature, vol. 457, 675-677, 2009. doi:10.1038/457675a
  Astrocyte enwraps many (~105) synapses and can connect to multiple (~6-8) neighbouring neurons.
  The connection between the astrocyte and neurons is named the tripartite synapse.
  When an action potential (AP) arrives at the presynaptic axon how do we describe the interactions between the neurons, synapses and astrocyte?
  Astrocyte-Neuron (AN) Model

## Slide 36: More Knowledge on Brain Repair
  Nicola J. Allen & Ben A. Barres, "Glia — more than just brain glue," Nature, vol. 457, 675-677, 2009. doi:10.1038/457675a
  Astrocyte enwraps many (~105) synapses and can connect to multiple (~6-8) neighbouring neurons.
  The connection between the astrocyte and neurons is named the tripartite synapse.
  When an action potential (AP) arrives at the presynaptic axon how do we describe the interactions between the neurons, synapses and astrocyte?
  Astrocyte-Neuron (AN) Model
1
2
3

## Slide 37: Software Model (AN) - A tripartite synapse story
  Action potential (Spike) - presynaptic axon
  Neuro-transmitter (Glutamate) is released across the cleft and binds to the receptors of the postsynaptic terminal.
Glu
  After depolarization of postsynaptic neuron, a type of endocannabinoid (2-AG) is synthesized and released from dendrite. 2-AG feeds back to the pre-synaptic terminal in two ways:
2-AG
2-AG
  Directly
  2-AG binds directly to the type 1 Cannabinoid Receptors (CB1Rs) of the presynaptic terminal.
  This causes a decrease of transmission probability rate (PR) of the synapses, and is termed Depolarization-induced Suppression of Excitation (DSE).
  Indirectly
  2-AG binds to CB1Rs of the astrocyte cell.
Direct feedback (DSE)
Decreasing the PR
IP3
  Increasing the IP3 level
Ca2+
  Triggers the release of calcium (Ca2+)
Glu
  Releases the glutamate (Glu) and binds to the receptors in the synapse
  Termed e-SP, this results in an increase of synapse probability of release (PR).
Indirect feedback (e-SP)
Increasing the PR
  J. Wade, L. McDaid, J. Harkin, et. al, “Self-Repair in a Bidirectionally Coupled Astrocyte-Neuron (AN) System based on Retrograde Signalling,” Frontiers in Computational Neuroscience, 6(76), pp. 1–12, 2012.
Endoplasmic Reticulum (ER)
Indirect F\B
(+)
Direct F\B
(-)
Probability
of
Release
(PR)
1
2
3

## Slide 38
Probability of Release
  J. Wade, L. McDaid, J. Harkin, et. al, “Self-Repair in a Bidirectionally Coupled Astrocyte-Neuron (AN) System based on Retrograde Signalling,” Frontiers in Computational Neuroscience, 6(76), pp. 1–12, 2012.
  Synapse model:
  rand is between 0 and 1.
  Iinj is a fixed current injected to the neuron.
  Probability of Release (PR)
  DSE (-): decreasing the PR.
  eSP (+): increasing the PR.

## Slide 39: The Bigger Picture - “Astro-Neuron Network”
  Action potential - presynaptic axon
  Neuro-transmitter (Glutamate) is released across the cleft and binds to the receptors of the postsynaptic terminal.
  After depolarization of postsynaptic neuron, a type of endocannabinoid (2-AG) is synthesized and released from dendrite. 2-AG feeds back to the pre-synaptic terminal in two ways:
  Directly
  2-AG binds directly to the type 1 Cannabinoid Receptors (CB1Rs) of the presynaptic terminal.
  Indirectly
  2-AG binds to CB1Rs of the astrocyte cell.
(Calcium signal broadcast) IP3
  J. Wade, L. McDaid, J. Harkin, et. al, “Self-Repair in a Bidirectionally Coupled Astrocyte-Neuron (AN) System based on Retrograde Signalling,” Frontiers in Computational Neuroscience, 6(76), pp. 1–12, 2012.
Many synapses to one Astrocyte
Multiple synapses

## Slide 40: The Bigger Picture - “Astro-Neuron Network”
  Action potential - presynaptic axon
  Neuro-transmitter (Glutamate) is released across the cleft and binds to the receptors of the postsynaptic terminal.
  After depolarization of postsynaptic neuron, a type of endocannabinoid (2-AG) is synthesized and released from dendrite. 2-AG feeds back to the pre-synaptic terminal in two ways:
  Directly
  2-AG binds directly to the type 1 Cannabinoid Receptors (CB1Rs) of the presynaptic terminal.
  Indirectly
  2-AG binds to CB1Rs of the astrocyte cell.
(Calcium signal broadcast) IP3
Many synapses to one Astrocyte
  J. Wade, L. McDaid, J. Harkin, et. al, “Self-Repair in a Bidirectionally Coupled Astrocyte-Neuron (AN) System based on Retrograde Signalling,” Frontiers in Computational Neuroscience, 6(76), pp. 1–12, 2012.
PR+
PR=0
PR+
Multiple synapses

## Slide 41: Self-repair of a ‘Small’ Astrocyte-Neuron Network
Neuron #2 under 80% fault rate with temporary faults.
(80% - severely damaged)
Temporary Faults injected
PR of Synapse #1
PR of Synapse #10
Faults (PR=~0)
Naeem M, McDaid L, Harkin J, Wade J, Marsland J, “On The Role of Astroglial Syncytia in Self-Repairing Spiking Neural Networks”, IEEE Transactions Neural Networks & Learning Systems, 2015.

## Slide 42: Self-repair of a ‘Small’ Astrocyte-Neuron Network
Neuron #2 under 80% fault rate with temporary faults.
(80% - severely damaged)
Temporary Faults injected
PR of Synapse #1
PR of Synapse #10
Faults (PR=~0)
Naeem M, McDaid L, Harkin J, Wade J, Marsland J, “On The Role of Astroglial Syncytia in Self-Repairing Spiking Neural Networks”, IEEE Transactions Neural Networks & Learning Systems, 2015.

## Slide 43: The Bigger Picture - “Astro-Neuron Network”
Astrocytes are the key player in how brain performs distributed repair.
What do Astrocyte-neuron networks afford?
Increased reliability via:
Fine-grained repair at synapse-level
Distributed repair mechanism (astrocyte cell)
New type of neural network paradigm?

## Slide 44: Goal and Challenges
On-chip interconnect: High levels of connections, different time scales, different data – spike events, numeric data values (increased interconnect problem due to astrocyte connections – scalability solutions required)
Tool-chain: Tools to map application to network paradigm, program the hardware, fault injection, data analysis and visualisation.
Tool-chain
Inter-connect
Blocks
Goal - Effectively map astrocyte-neuron networks to hardware (i.e. reliability via self-repair).
Model real applications: Larger networks.
Key functional blocks: Astrocyte, tri-partitie synapse and learning rule (trade-off computational complexity for key principle with area/power efficiency)

## Slide 45
Brain-inspired Hardware
Reliability via Self-repair (the concept)
Building Self-repairing Hardware
On-chip Communication Challenge and NoC Solution
Reliability Challenge
The Opportunities
Brain-inspired Information Processing

## Slide 46: Proof-of-Principle: Moving to Hardware
First-principle computer model of brain-like repair (Astrocyte-neuron Networks).
Explored the mapping to hardware as it enables repairs to achieved when the underlying hardware is unreliable.

## Slide 47: SPANNER: Moving to Hardware
Synapse facility
Neuron facility
Astrocyte facility
Current
DSE
2-AG
e-SP
DSE
2-AG
e-SP

## Slide 48: FPGA Hardware Implementation
  Astrocyte-neuron network with 2 neurons (N1, N2), 20 synapses (C1, C2), and 1 astrocyte cell (A).
  Xilinx Virtex-7 XC7VX485T
  Vivado High Level Synthesis tool to generate the IP blocks
  Xilinx VC707 development board
Neuron #2
Neuron #1

## Slide 49: ‘Small’ Astrocyte-Neuron Network to FPGAs
  Liu J, Harkin J, Maguire LP, McDaid L, Wade J; "Self-Repairing Hardware with Astrocyte-Neuron Networks", IEEE International Symposium on Circuits and Systems, Canada (ISCAS), May 23rd-25th, 2016
  1 astrocyte, 2 neurons (20 synap.)
  Neuron #1
  (blue)
  Neuron #2
  (red)
  Xilinx Virtex-7 XC7VX485T

## Slide 50: ‘Small’ Astrocyte-Neuron Network to FPGAs
  Liu J, Harkin J, Maguire LP, McDaid L, Wade J; "Self-Repairing Hardware with Astrocyte-Neuron Networks", IEEE International Symposium on Circuits and Systems, Canada (ISCAS), May 23rd-25th, 2016
  1 astrocyte, 2 neurons (20 synap.).
  Neuron #1
  (blue)
  Neuron #2
  (red)
Graceful degradation
80% damage injected
Synapse #1
Synapse #10
  Xilinx Virtex-7 XC7VX485T

## Slide 51: Apply to mobile robotic car
Normal state
Faults injected
  IEEE International Symposium on Circuits and Systems, Canada (ISCAS), May 23rd-25th, 2016

## Slide 52: ‘Small’ Astrocyte-Neuron Network to FPGAs
  Liu J, Harkin J, Maguire LP, McDaid L, Wade J; "Self-Repairing Hardware with Astrocyte-Neuron Networks", IEEE International Symposium on Circuits and Systems, Canada (ISCAS), May 23rd-25th, 2016
  Xilinx Virtex-7 XC7VX485T
Implementation | Time [sec]
Biological neural network | 600
Software simulation | 64
FPGA | 7

## Slide 53: Challenges
On-chip interconnect: High levels of connections, different time scales, different data – spike events, numeric data values (increased interconnect problem due to astrocyte connections – scalability solutions required)
Tool-chain: Tools to map application to network paradigm, program the hardware, fault injection, data analysis and visualisation.
Tool-chain
Inter-connect
Blocks
Model real applications: Larger networks.
Key functional blocks: Astrocyte, tri-partitie synapse and learning rule (trade-off computational complexity for key principle with area/power efficiency)

## Slide 54: Acceleration Platform
We incorporate Astrocyte cell into SNNs i.e. the ability of self-repair.
Therefore, network simulations even more complex.
FPGAs acceleration can reduce the simulation time.
Recently dedicated simulation accelerators
  GPU Accelerators (NeMo)
  Custom Processor accelerators (BrainScales2)
FPGA Accelerators:
SpiNNaker 1 Million Cores…
IBM TrueNorth
NTU

## Slide 55
Key Research Problem
How to implement large-scale accelerators on a multiple FPGA platform and send/receive data from the platform easily ?
Requires the system to achieve:
  More area efficient astrocyte cells.
  Monitoring and exchanging data with the multiple FPGA platform.
  Interconnect (NoC) to channel information (inter/intra FPGA).

## Slide 56
56
The Astrocyte model implemented based on original block functions.
Refining Astrocyte Hardware
Astrocyte hardware is faithful to the original model.
Each block is sub-function in the original model.
Equations belonging to each sub-function were realized using VHDL: 32-bit fixed point (8-bit real, 24-bit fractional).
Differential equations represented using Euler method.
An Euler constant of 0.001 seconds was used.
S. Karim, J Harkin, LJ McDaid et al., “Assessing Self-Repair on FPGAs with Biologically Realistic Astrocyte-Neuron Networks,” Proc. IEEE Computing Society Annual Symposium on VLSI (ISVLSI), July, pp. 421–426, 2017

## Slide 57
57
Astrocyte Precision Analysis
Accuracy compared against double float Matlab implementation.
24 bit precision results in more than 10% loss in accuracy.
40-bit precision significantly increases FPGA resource usage without improving accuracy to any degree.
32 bit precision was a reasonable trade-off between resource usage and accuracy..
24-bit
32-bit
S. Karim, J Harkin, LJ McDaid et al., “Assessing Self-Repair on FPGAs with Biologically Realistic Astrocyte-Neuron Networks,” Proc. IEEE Computing Society Annual Symposium on VLSI (ISVLSI), July, pp. 421–426, 2017

## Slide 58
Fault-injection and Data Monitoring (FMP)
Shvan Karim, Jim Harkin, Liam McDaid, Bryan Gardiner, Junxiu Liu, David M Halliday, Andy M Tyrrell, Jon Timmis, Alan G Millard, Anju P Johnson
"FPGA-based Fault-injection and Data Acquisition of Self-repairing Spiking Neural Network Hardware", IEEE International Symposium on Circuits and Systems (ISCAS) 2018
Fault-injection and Data Acquisition Platform for FPGA-based Astrocyte-Neuron Networks

## Slide 59
Shvan Karim, Jim Harkin, Liam McDaid, Bryan Gardiner, Junxiu Liu, David M Halliday, Andy M Tyrrell, Jon Timmis, Alan G Millard, Anju P Johnson
"FPGA-based Fault-injection and Data Acquisition of Self-repairing Spiking Neural Network Hardware", IEEE International Symposium on Circuits and Systems (ISCAS) 2018
Fault-injection and Data Acquisition Platform for FPGA-based Astrocyte-Neuron Networks
Fault-injection and Data Acquisition (FMP)

## Slide 60
60
(reducing PR from 0.5 to zero)
(reducing PR from 0.5 to 0.1)
Faults were injected at specific time during the simulation.
Faults severe (reducing PR from 0.5 to zero) or partial (PR 0.50.1).
N1 and N2 have the similar avg. O/P frequency up to severe faults injected.
Partial fault
Spiking rate reduces gradually to rates of partial faults.
Severe fault
Spiking rate reduces more steeply to rates of severe faults.
Experiments on Graceful Degradation

## Slide 61
Speedup of Network Simulations
If 1 in every 10 samples are recorded - overall simulation and acquisition time will be reduced from around 724 seconds to ~63 seconds.
Under-sampling
Speedup factor between x50 - 65
Communication bottleneck challenge
Acceleration Factor (Matlab Vs FPGA)
Shvan Karim, Jim Harkin, Liam McDaid, Bryan Gardiner, Junxiu Liu, David M Halliday, Andy M Tyrrell, Jon Timmis, Alan G Millard, Anju P Johnson
"FPGA-based Fault-injection and Data Acquisition of Self-repairing Spiking Neural Network Hardware", IEEE International Symposium on Circuits and Systems (ISCAS) 2018

## Slide 62: Challenges
On-chip interconnect: High levels of connections, different time scales, different data – spike events, numeric data values (increased interconnect problem due to astrocyte connections – scalability solutions required)
Tool-chain: Tools to map application to network paradigm, program the hardware, fault injection, data analysis and visualisation.
Tool-chain
Inter-connect
Blocks
Model real applications: Larger networks.
Key functional blocks: Astrocyte, tri-partitie synapse and learning rule (trade-off computational complexity for key principle with area/power efficiency)

## Slide 63
Brain-inspired Hardware
Reliability via Self-repair (the concept)
Building Self-repairing Hardware
On-chip Communication Challenge and NoC Solution
Reliability Challenge
The Opportunities
Brain-inspired Information Processing

## Slide 64: Interconnect Challenge
  Large volumes of neurons\astrocytes with different communication requirements:
  high speed temporal spike event for the neuron network
  low speed numerical inositol trisphosphate () information exchange for astrocyte network
  Astrocyte-neuron network viewed as two-tiered network (neuron and astrocyte networks).

## Slide 65: Background: Evolution Timeline
Xilinx Versal FPGA

## Slide 66
On-chip Interconnection
Bus-based was Traditional
P1
I/O
2
P2
P3
M1
P4
M2
I/O
1
P5
P6
M3
I/O
3
P7
M4
Wait
Wait
Wait
Wait
Wait
Wait
Notes: To overcome wiring or interconnect complexity Bus based system was proposed .
It is easy to set up, handle, understand and implement.
It is best-suited for small networks.
while the number of components attached to the bus is increased, a physical capacitance on the bus wires grow.
As a result its wiring delay grows even further causing propagation delays.

## Slide 67: Bus-based communication

## Slide 68: Introduction to NoC - Basic Components
  What is Networks-on-Chip (NoC) ???
      New interconnection paradigm that is used to connect electronic systems inside a chip
  Why do we need it ???
      Number of transistors (Moore’s Law)
      Modularity (IP cores + re-used)
      Reduce time to market

## Slide 69
Networks-on-Chip (NoC)
Mesh Based
Router
Processing Element
Network Interface
Communication Data
Notes: To overcome the deficiencies of scalability and latency network on chip (NoC) architecture has been adopted. It provides Point-to-point contact between every pair of nodes with bus based wiring system, in which one channel is used by multiple processor. This approach has the tendency to fulfil high performance requirements and it provides the designers with multi-path options to optimize their design according to their requirement.
NoC use routing algorithm to deliver data from source to destination node. an ideal routing algorithm the traffic will be evenly distributed in the network,
Congestion/hotspot is caused by the concentration of traffic in a network area producing a slow-down in data communication while other links are free elsewhere.
The arrangement of the network nodes is such that it is possible to transmit data from one node to many other nodes at the same time
By applying network-like communication which inserts some routers in-between each communication object, the required wiring can be shortened. Therefore, the switch-based interconnection mechanism provides a lot of scalability and freedom from the limitation of complex wiring.

## Slide 70: Messaging Units
Data is transmitted based on a hierarchical data structuring mechanism
  Messages  packets  flits  phits
  flits and phits are fixed size, packets and data may be variable sized
  phit is a unit of data that is transferred on a link in a single cycle
  typically, phit size = flit size
Data/Message
Head flit
Flits: flow control digits
Phits: physical flow control digits
Packet
Dest Info
Seq #
misc
Tail flit
type
70
Packet
Packet
Packet
Flit
Flit

## Slide 71: NoC – Its Abstraction and Challenges
  NoC Advantages…
    Scalability
    Modularity
    High level abstraction
  NoC Challenges…
    Design efficient routers
    Hierarchical topologies
    Routing Algorithms

## Slide 72: NoC Interconnect Scalability
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
3x3 array
5x5 array
8x8 array

## Slide 73: NoC Concepts
NoC Architecture (a.k.a. NoC router)
  Combinational and sequential components
Topology
  How the nodes are connected together
Routing Algorithms
  Path selection between a source and a destination node in a particular topology
Switching Mechanisms
  Allocation of network resources (bandwidth, buffer capacity, …) to information flows
Flow control Mechanisms
  How the downstream node communicates forwarding availability to the upstream node

## Slide 74: NoC Concepts
NoC Architecture (a.k.a. NoC router)
  Combinational and sequential components
Topology
  How the nodes are connected together
Routing Algorithms
  Path selection between a source and a destination node in a particular topology
Switching Mechanisms
  Allocation of network resources (bandwidth, buffer capacity, …) to information flows
Flow control Mechanisms
  How the downstream node communicates forwarding availability to the upstream node

## Slide 75: Generic NoC Router Architecture
RC
VCA
SA
ST
LT
Router
Link
LT: Link Traversal
RC: Route Computation
VCA: VC Allocation
SA: Switch Allocation
ST: Switch Traversal.
By using prediction/speculation, pipeline can be made more compact

## Slide 76: Pipelined Router Microarchitecture
CrossBar
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
VC Allocation
LT & IB (Input Buffering)
RC
VCA
SA
ST & Output Buffering
Input buffers
Input buffers
DEMUX
Physical
channel
Link
Control
Link
Control
Physical
channel
MUX
DEMUX
MUX
Output buffers
Link
Control
Output buffers
Link
Control
Physical
channel
Physical
channel
DEMUX
MUX
DEMUX
MUX
Routing Computation
Routing Computation
Switch Allocation

## Slide 77: NoC Topologies

## Slide 78: NoC Topologies
  Mesh
  Torus
  Binary-Tree
  Star
  Hybrid
  Ring

## Slide 79: Abstract Metrics: Degree
79

## Slide 80: Abstract Metrics: Hop Count
80

## Slide 81: Abstract Metrics: Path Diversity
81

## Slide 82: Unconventional NoC Topologies
82

## Slide 83: NoC Concepts
NoC Architecture (a.k.a. NoC router)
  Combinational and sequential components
Topology
  How the nodes are connected together
Routing Algorithms
  Path selection between a source and a destination node in a particular topology
Switching Mechanisms
  Allocation of network resources (bandwidth, buffer capacity, …) to information flows
Flow control Mechanisms
  How the downstream node communicates forwarding availability to the upstream node

## Slide 84: Taxonomy for Routing Algorithms
Routing algorithm determines the path selection by a packet to reach its destination
  A routing algorithm aims to balance traffic loads to maximise throughput of data packets

## Slide 85: Static vs. Dynamic Routing
Static routing: fixed paths are used to transfer data between source & destination
    does not take into account current state of the network
advantages of static routing:
    easy to implement, since very little additional router logic is required
    in-order packet delivery if single path is used
Dynamic routing: routing decisions are made according to the current state of the network
    considering factors such as availability and load on links
path between source and destination may change over time
    as traffic conditions and requirements of the application change
more resources needed to monitor network state and dynamically change routing paths
able to better distribute traffic in a network
85

## Slide 86: Example: Static Routing
Static XY routing (commonly used):
a deadlock-free shortest path routing which routes packets in the X-dimension first and then in the Y-dimension.
Used for tori and meshes
Destination address expressed as absolute coordinates
00
10
20
01
11
21
02
12
22
03
13
23
-x
+y
(1,1) – (2,0)  -X
(1,1) – (1,0)  +Y
(1,1) – (1,1)  FD

## Slide 87: Example: Adaptive Routing
Chooses shortest path to destination with minimum congestion
  Path can change over time
    Because congestion changes over time
00
10
20
01
11
21
02
12
22
03
13
23

## Slide 88: The Livelock Problem
  The Livelock problem !!…
    Livelock occurs when a packet travels indeﬁnitely in the network without ever reaching its destination.
    Possible solution: a counter !!!

## Slide 89: NoC Concepts
NoC Architecture (a.k.a. NoC router)
  Combinational and sequential components
Topology
  How the nodes are connected together
Routing Algorithms
  Path selection between a source and a destination node in a particular topology
Switching Mechanisms
  Allocation of network resources (bandwidth, buffer capacity, …) to information flows
Flow control Mechanisms
  How the downstream node communicates forwarding availability to the upstream node

## Slide 90: Switching Techniques
  The Switching techniques can be classified based on…
    Circuit switched networks reserve a physical path before transmitting the data packets.
    packet switched networks transmit the packets without reserving the entire path.
  A switching technique determines the way a packet is transmitted across the network…

## Slide 91: Circuit Switching
Setup Time (negotiation)
Source
end node
Destination
end node
Buffers
for “request”
tokens

## Slide 92: Circuit Switching
Setup Time (negotiation)
Request for circuit establishment
(routing and arbitration is performed during this step)
Source
end node
Destination
end node
Buffers
for “request”
tokens

## Slide 93: Circuit Switching
Setup Time (negotiation)
Request for circuit establishment
Source
end node
Destination
end node
Buffers
for “ack” tokens
Acknowledgment and circuit establishment
(as token travels back to the source, connections are established)

## Slide 94: Circuit Switching
Data Transmission
Request for circuit establishment
Source
end node
Destination
end node
Acknowledgment and circuit establishment
Packet transport
(neither routing nor arbitration is required)

## Slide 95: Packet Switching
Packets are transmitted from source and make their way independently to receiver
  possibly along different routes and with different delays
Zero start up time, followed by a variable delay due to contention in routers along packet path
  QoS guarantees are harder to make
Three main packet switching scheme variants:
  Store and Forward (SAF) switching
  Virtual Cut Through (VCT) switching
  Wormhole (WH) switching
95

## Slide 96: Packet Switching (Store & Forward)
Source
end node
Destination
end node
Packets are completely stored before any portion is forwarded
Store
Buffers
for data
packets
Message Header
tpacket
Link
Message Data
tr
Time Busy

## Slide 97: Packet Switching (Store & Forward)
Source
end node
Destination
end node
Packets are completely stored before any portion is forwarded
Store
Forward
Requirement:
buffers must be
sized to hold
entire packet
(MTU)
Message Header
tpacket
Link
Message Data
tr
Time Busy

## Slide 98: Packet Switching (Virtual Cut-through)
Source
end node
Destination
end node
Routing
Portions of a packet may be forwarded (“cut-through”) to the next switch
before the entire packet is stored at the current switch

## Slide 99: Virtual Cut Through vs. Wormhole
Virtual Cut Through
Wormhole
Source
Destination
end node
Source
Destination
Buffers for data
packets
Requirement:
buffers must be sized
to hold entire packet
(MTU)
Buffers for flits:
packets can be larger
than buffers

## Slide 100: Virtual Cut Through vs. Wormhole
Destination
end node
Source
Destination
Busy
Link
Packet stored
along the path
Busy
Link
Packet completely
stored at
the switch
Buffers for data
packets
Requirement:
buffers must be sized
to hold entire packet
(MTU)
Buffers for flits:
packets can be larger
than buffers
Virtual Cut Through
Wormhole

## Slide 101: Evaluation Metrics
  Throughput  frequency operation, number of pipeline stages, etc…
  Latency  routing algorithm, switching technique, packet format, etc…
  Area Utilisation  buffers, look-up tables, routing engine, CMOS technology etc…
  Power Consumption  throughput spec + latency spec + area spec !!!
Trade-Off !!

## Slide 102: NoC for Brain Info. Communication?
  Hierarchical NoC (H-NoC) for spiking neural network: Neuron, Tile & Cluster levels.
Hierarchical Astrocyte Network Architecture (HANA)
Liu J, Harkin J, McDaid L, Martin G; "Hierarchical NoC Interconnect for Astrocyte-Neuron Network Hardware", 25th Inter. Conf. on Artificial Neural Nets (2016)
10-3 sec. timescale
101 sec. timescale
  Carrillo, S., Harkin, J., McDaid, et. al: “Scalable Hierarchical NoC Architecture for Spiking Neural Network Hardware Implementations”. IEEE Trans. on Parallel and Distributed Systems. (2013)

## Slide 103: NoC for Brain Info. Communication?
  Hierarchical NoC (H-NoC) for spiking neural network: Neuron, Tile & Cluster levels.
  Carrillo, S., Harkin, J., McDaid, et. al: “Scalable Hierarchical NoC Architecture for Spiking Neural Network Hardware Implementations”. IEEE Trans. on Parallel and Distributed Systems. (2013)
Hierarchical Astrocyte Network Architecture (HANA)
Martin G J, Harkin J, McDaid L et al. "On-chip communication for neuro-glia networks" IET Computers & Digital Techniques, 12(4), pp. 130-138, 7 2018
10-3 sec. timescale
101 sec. timescale

## Slide 104: NoC for Brain Info. Communication?
  Hierarchical NoC (H-NoC) for spiking neural network: Neuron, Tile & Cluster levels.
  Carrillo, S., Harkin, J., McDaid, et. al: “Scalable Hierarchical NoC Architecture for Spiking Neural Network Hardware Implementations”. IEEE Trans. on Parallel and Distributed Systems. (2013)
Hierarchical Astrocyte Network Architecture (HANA)
10-3 sec. timescale
101 sec. timescale
Ring topology
Martin G J, Harkin J, McDaid L et al. "On-chip communication for neuro-glia networks" IET Computers & Digital Techniques, 12(4), pp. 130-138, 7 2018

## Slide 105: NoC Works!
  Hierarchical NoC (H-NoC) for spiking neural network: Neuron, Tile & Cluster levels.
  Carrillo, S., Harkin, J., McDaid, et. al: “Scalable Hierarchical NoC Architecture for Spiking Neural Network Hardware Implementations”. IEEE Trans. on Parallel and Distributed Systems. (2013)
Hierarchical Astrocyte Network Architecture (HANA)
Liu J, Harkin J, McDaid L, Martin G; "Hierarchical NoC Interconnect for Astrocyte-Neuron Network Hardware", 25th Inter. Conf. on Artificial Neural Nets (2016)
Increased throughput under load testing
HNoC router performance

## Slide 106
Brain-inspired Hardware
Reliability via Self-repair (the concept)
Building Self-repairing Hardware
On-chip Communication Challenge and NoC Solution
Reliability Challenge
The Opportunities
Brain-inspired Information Processing

## Slide 107: What is Next?
  Major potential gains in the provision of adaptive systems that provide high-levels of reliability.
  New generation of engineers required to think differently!
  Exploring beyond information processing brings new models of reliable computation. Engineering and Neuroscience?
  Next big wave in how we design modern embedded systems.

## Slide 108: Opportunities
  Build new computers that allow Neuroscientists to understand brain diseases (e.g. Parkinson's), pharmaceutical companies design new drugs.
  Harsh environments: Robotics in nuclear industry, Wireless sensor networks in environmental disasters; forest fire, structural health monitors (earthquake damage).
  Remote locations: Border security, Space, Deep sea
  Error resilience in computing: Plastic electronics, robotics, modern microprocessors

## Slide 109: Opportunities
???
Augment existing architectures – not replace!
  Build new computers that allow Neuroscientists to understand brain diseases (e.g. Parkinson's), pharmaceutical companies design new drugs.
  Harsh environments: Robotics in nuclear industry, Wireless sensor networks in environmental disasters; forest fire, structural health monitors (earthquake damage).
  Remote locations: Border security, space, deep sea
  Error resilience in computing: Plastic electronics, robotics, modern microprocessors.

## Slide 110: Take Home Message
  Embedded AI - many challenges remaining
  Astrocyte Neuron systems - Disruptive approach
  Major potential gains in the provision of adaptive systems that provide high-levels of reliability
  Feasibility shown for establishing future development
  EPSRC SPANNER project (EP/N00714X/1)
  Modelling: Prof. L McDaid, Dr J Wade Dr B Flanagan (A Reza, D Harkin)
  Hardware: Dr J Harkin, Dr J Liu, M. McElholm, Dr G Martin (A Javid, D Simpson, N Hamilton, K Madden)
Computational Neuroscience and Neuromorphic Engineering Team
  Human Frontiers Science Programme

## Slide 111: Thank You
  Modelling: Prof. L McDaid, Dr J Wade Dr B Flanagan (A Reza, D Harkin)
  Hardware: Dr J Harkin, Dr J Liu, M. McElholm, Dr G Martin (A Javid, D Simpson, N Hamilton, K Madden)
  Human Frontiers Science Programme
  EPSRC SPANNER project (EP/N00714X/1)